## Slide 1: Emissions Modeling
Daniel Tong
UMD CICS / NOAA ARL
June 22, 2016

## Slide 2
Emissions Modeling
Emissions Inventories
Model-ready Emission
Real World Emissions
Air Quality Forecast
Meteorology Forecast
Emission Forecast

## Slide 3: Emissions for Air Quality Forecasting (AQF)
Time lag is a major obstacle for AQF
  Forecasters want: emissions for tomorrow
  Data availability: emissions data 4+ years old
How to overcome this problem?
NAQFC Practices:
  Option 1, no update (2007-2011)
  Option 2, use EPA projection (2012-2015)
  Option 3, emissions data assimilation (2016-)

## Slide 4
NAQFC Ozone Forecast
Peak 8h Ozone (ppb)
2009:
NEI Only
2012:
NEI with Projection
NEI: National Emissions Inventory
(Tong et al., 2015)

## Slide 5
Tropospheric NO2 Changes from OMI
2005
(OMI: Ozone Monitoring Instrument)
2012
Difference

## Slide 6
NOx Trends from OMI, AQS and NAQFC
Atlanta
Philadelphia
Comparison to 2005 values
OMI = Ozone Monitoring Instrument on NASA’s Aura Satellite
AQS = Air Quality System
OMI (Space)
AQS (Ground)
NAQFC (Model)
Philadelphia
Atlanta

## Slide 7
NOx Trends during the Great Recession
Consistent trends from OMI and AQS;
Faster NOx reduction during the Recession and slower after that.
(Tong et al., 2015)

## Slide 8
Rapid Refresh of NOx Emissions
8
Question: Can satellite and ground data be used to rapidly refresh NOx emissions?
Fusing AQS & OMI
Comparison of OMI and AQS (x100) Samples
State-level Projection Factors
(2005 to 2012)

## Slide 9
Effect of Using
EPA Projection
Effect of Using
Fused Obs.
Difference
Effect on O3 Forecast
Performance Metrics (July 2011 over CONUS)

## Slide 10: Weather Aware Emission: Snow/ice effect
?
Anthropogenic

## Slide 11
Dynamic Fire Emissions
Fire detection: NOAA Hazard Mapping System
ARL modifications for optimal performance
Emissions estimation: BlueSky
Aqua MODIS AOD
NAQFC PM2.5 Forecasting

## Slide 12
2013
Validation
NAQFC Hawaii Domain
Satellite Retrievals of Marine Emissions

## Slide 13
Blowing Dust Event -- PM2.5 Forecast
NOAA/NESDIS
HMS Dust Observations:
California/Arizona: An area of moderately/dense blowing dust was visible sweeping across northern Baja California/Arizona into western New Mexico behind a strong cold frontal boundary.

## Slide 14
Chinese Sand and Dust Network
The US Aerosol Network IMPROVE
(Wang et al., 2008)
Dust Observations to Verify Forecasts

## Slide 15
Satellite-aided Algorithm Development
GUMO
Apr. 15, 2003
GUMO
BIBE
Nov. 27, 2005
SAGO1
DEVA
Apr. 12, 2007
Crustal (mg/m3)

## Slide 16
GUMO
Apr. 15, 2003
GUMO
BIBE
Nov. 27, 2005
SAGO1
DEVA
Apr. 12, 2007
Satellite-aided Algorithm Development
PM2.5/PM10

## Slide 17: Identify Dust Storms - Cluster Analysis
PM10,PM2.5
Crustal Element Concentration
PM2.5/PM10
Enrichment Factor
Cu, Pb, Zn
Crustal Element Fraction
  High PM10, PM2.5
  Low PM2.5/PM10
  High Crustal Fraction
  Low Anthropogenic Fraction
  Low Enrichment Factor

## Slide 18: Dust Trend in the United States
Total: 204
Total: 480
Dust storms become more frequent

## Slide 19: Dust and Valley Fever
Coccidioidomycosis, commonly known as Valley Fever, is an infection caused by inhalation of a soil-dwelling fungus.
The incidence rate of valley fever has increased by eight-fold from 1998 in 2011 in the same regions where increased dust frequency is detected.
Valley Fever
Dust Region

## Slide 20: Dust Bowl: Threat to US Economy
Dust Bowl- One of the worst man-made catastrophes in US history
  Huge dust storms caused by droughts and poor land use
  Stripped 75% of top soils
  2 millions lost homes
  Destroyed agriculture (30s-50s)
Another Dust Bowl inevitable in late 21 st Century?
  Much drier conditions later this century (Cook et al., 2015)
  “Dust-bowlification” rather than desertification in the American subtropics (Romm, 2011)

## Slide 21: Dust for National Climate Assessment
The U.S. Global Change Research Program (USGCRP), mandated by the Global Change Research Act (1990), prepares a report to Congress every 3 years.
A key task of National Climate Assessment (NCA) is to develop a suite of climate indicators (physical, ecological, and societal).
NCA Dust Climate Indicator
Baseline
Trend
Climate drivers
Predictability

## Slide 22
Quality
Publications
28 publications in peer-reviewed journals (2011-2016)
Reimbursable Support
NOAA Joint Polar Satellite System (2012-2015)
NASA ROSES & USGCRP (2012-2014)
NSF EarthCube Initiative (2014-2016)
US Weather Research Program (2015-2016)
NASA ROSES & USGCRP (2016-2018)
NOAA US Weather Research Program (2016-2019)
NOAA Climate Program Office AC4 (2017-2019)
Award
USEPA Scientific & Technological Achievement Awards

## Slide 23: Summary
Advance emissions science to support NOAA chemical weather forecasts
Produce high-quality emission products to serve the community at large
Emissions rapid refreshing capability
Weather-aware emissions
Intermittent emission sources (dust, fire, etc.)
Products to support field campaigns (NASA, NOAA and NSF)
Satellite products of marine emissions
Dust records for national climate assessment